## Slide 1
The Art of Error Correcting Coding
Speaker: Y. H. Chen

## Slide 2: Agenda
Reed-Solomon Codes Using Algorithm for Encoder and Decoder
Decoding Binary Quadratic Residue Codes

## Slide 3: Reed-Solomon Codes Using Algorithm for Encoder and Decoder

## Slide 4: Outline
Introduction
Mathematics Background
Reed-Solomon Code
Software Simulation
Design of Critical modules
Hardware Implementation and Test
Conclusion

## Slide 5: Introduction
Application
  DVD, HDTV, CD-ROM, Space Communication
Hardware Modules
  Multiplier, Syndrome, Berlkamp Massey, Chien search, Correction and Inverse modules.

## Slide 6: Mathematics Background
Algebraic Structure
  Groups, closure, associatively, identity, inverse
Galois Fields
  q elements in the Finite field
Polynomial Algebra
  Example of

## Slide 7: The Reed-Solomon Code
Encode
  if an (n, k) code

## Slide 8: For example
Galois field, GF(16)=GF( )
  {0,1,2,3,4,5,6,7,8,9,10,11,12,13,14,15}
Symbol
  m=4 is 4bits symbol
  0 -> 0001, 4 ->0011, 8 ->0101, 12->1111
  1 -> 0010, 5 ->0110, 9 ->1010, 13->1101
  2 -> 0100, 6 ->1100, 10->0111, 14->1001
  3 -> 1000, 7 ->1011, 11->1110,

## Slide 9: Encode (15,9) RS code
9 symbols, I(x)
9 message symbols
6 parity check symbols
g(x)
C(x)

## Slide 10: The Decoding of Reed-Solomon Code
Decoder
Syndrome evaluation
Error locator polynomial
Chien search
Amplitude
evaluation
Data in
buffer
Data Correct
Correction
and Inversion
Peterson algorithm
Berlkamp Massey
algorithm
Euclidean algorithm

## Slide 11: The Implementation of Reed-Solomon Codes

## Slide 12: Software Simulation
Verifying RS Code algorithm step by step

## Slide 13: ..Software Simulation
Software to achieve hardware architecture
  Example Encode using LFSR
C2
C3
C1
g4
g3
g2
g1
C5
g6
C4
g5
C0
g0
I(X)
    C0=IX+C5*G6*G0
    C1=C0+C5*G6*G1
    C2=C1+C5*G6*G2
    C3=C2+C5*G6*G3
    C4=C3+C5*G6*G4
    C5=C4+C5*G6*G5
    NEXT_C0=IX+C5*G6*G0
    NEXT_C1=C0+C5*G6*G1
    NEXT_C2=C1+C5*G6*G2
    NEXT_C3=C2+C5*G6*G3
    NEXT_C4=C3+C5*G6*G4
    NEXT_C5=C4+C5*G6*G6
    Following statements are arouse by the colock.
    C0=NEXT_C0
    C1=NEXT_C1
    C2=NEXT_C2
    C3=NEXT_C3
    C4=NEXT_C4
    C5=NEXT_C5

## Slide 14: ..Software Simulation
The Functional Block Diagram
The top down design of RS decoder

## Slide 15: Design of The Critical Module
Serial multiplier
sequential logic
Parallel multiplier
combination logic
The comparison of different multipliers

## Slide 16: Design of The Critical Module
The FPGA Floorplan of Multipliers
Viewing serial multiplier in the Floorplan (FLEX 8000 EPF8282ACL84-4)
Viewing parallel multiplier in the Floorplan (FLEX 8000 EPF8282ACL84-4)
Total dedicated input pins used: 4/4 (100%)
Total I/O pins used: 10/64 ( 15%)
Total logic cells used: 12/208 ( 5%)
propagation 14ns
Total dedicated input pins used: 4/4 (100%)
Total I/O pins used: 10/64 ( 15%)
Total logic cells used: 9/208 ( 4%)
clock 125MHZ

## Slide 17: Design of The Critical Module
Timing Requirement
4bit serial multiplier waveform
4bit parallel multiplier waveforms

## Slide 18: Design of The Critical Module
Inversion circuit design

## Slide 19: Hardware Implementation and Test
Syndrome evaluation circuit
.
.
.

## Slide 20: Hardware Implementation and Test
Total dedicated input pins used: 6/6 (100%)
Total I/O pins used: 24/183 ( 13%)
Total logic cells used: 24/4992 ( 0.004%)
clock 125 Mhz
15 clocks for Syndrome

## Slide 21: Hardware Implementation and Test
Inversionless Berlekamp Massey circuit
Where C are the coefficients of error locator polynomial

## Slide 22: Hardware Implementation and Test
BM Control module
Timing Analysis
SUBDESIGN BM_CTRL
(
CLKIN :INPUT;
CLEAR :INPUT;
DELETA[3..0] :INPUT;
CLK[3..1] :OUTPUT;
COUNT[3..0] :OUTPUT;
NL[3..0] :OUTPUT;
SELA :OUTPUT;
GAMAR[3..0] :OUTPUT;
)
VARIABLE
CLK1 :DFF;
COUNT[3..0] :DFF;
SELA :DFF;
NL[3..0] :DFF;
GAMAR[3..0] :DFF;
TEMP[4..0] :NODE;
BEGIN
% CLS %
CLK1.CLK = CLKIN;
CLK2 = !CLK1.Q;
CLK1.D = CLK2;
CLK3 = (!CLKIN & (clk1 # !SELA));
% CLOCK %
SELA.PRN = CLEAR;
GAMAR0.PRN = CLEAR;
COUNT[].CLRN = CLEAR;
NL[].CLRN = CLEAR;
CLK1.CLRN = CLEAR;
GAMAR[3..1].CLRN = CLEAR;
% MAKE UP %
COUNT[].CLK = CLK1.Q;
SELA.CLK = CLKIN;
NL[].CLK = CLKIN;
GAMAR[].CLK = CLKIN;
COUNT[] = COUNT[] +1;
% GAMAR && SELAIO%
TEMP[] = (NL[],0);
IF ((DELETA[] != 0) & (TEMP[]<=(0,(count[]-1)))) THEN
GAMAR[].D = DELETA[];
NL[] = COUNT[] - NL[];
ELSE
GAMAR[].D = GAMAR[].Q;
NL[].D = NL[].Q;
END IF;
IF ((DELETA[] != 0) & (TEMP[]<=(0,(count[]-1)))
& (CLK1 != 0) & (SELA != 0))THEN
SELA = GND;
ELSE
SELA = VCC;
END IF;
END;

## Slide 23: Hardware Implementation and Test
Total dedicated input pins used: 6/6 (100%)
Total I/O pins used: 52/183 ( 28%)
Total logic cells used: 361/4992 ( 7%)
13 clocks for BM

## Slide 24: Hardware Implementation and Test
Polynomial Evaluation and Chien search
Forncy’s algorithm
15 clocks for Chien search need

## Slide 25: Hardware Implementation and Test
Buffer
Integrated and pipelined issues
  Numbers of registers for delay buffers are in system
  Timing control in system

## Slide 26: Hardware Implementation and Test

## Slide 27: Hardware Implementation and Test
Timing requirements

## Slide 28: Hardware Implementation and Test
4bit decoder in the floorplan
(FELX10K EPF100KRI240-3)
Total dedicated input pins used: 2/6 (33%)
Total I/O pins used: 100/183 ( 54%)
Total logic cells used: 705/4992 ( 14%)

## Slide 29: The Prototyping System

## Slide 30: Random Testing

## Slide 31: Image Testing

## Slide 32: Conclusion
Improved Design Methodology Using Codesign
  Windows, Simulator, Emulator
Critical Modules Improvement
  Multiplier, Inversion
Efficient system development
  Supports of testBench promote the level of the system development

## Slide 33: Decoding Binary Quadratic Residue Codes

## Slide 34: Outline
Introduction
Conceptual Framework
Methodology of Study
The Algebraic Decoding of Some Quadratic Residue (QR) Codes
Conclusions

## Slide 35: (1) Introduction
QR codes have two nice properties:
  Block codes.
  Algebraically decodable.
QR codes are very good codes to use for concatenated codes.
QR codes are cyclic codes.
The QR codes have large minimum distances.

## Slide 36: A Concatenated Code

## Slide 37: Interleaving
Codeword
Codeword

## Slide 38: New Concatenated Code

## Slide 39: Large Minimum Distances
(7, 4, 3)
0000 000
0001 011
0010 110
0011 101
0100 111
0101 100
0110 001
0111 010
1000 101
1001 110
1010 011
1011 000
1100 010
1101 001
1110 100
1111 111

## Slide 40: Conceptual Framework
Let n be a prime number of the form n=8l±1, where l is a positive integer..
The set of quadratic residues modulo n is the set of nonzero squares modulo n; that is

## Slide 41: Conceptual Framework
A binary (n, k, d) QR code is a cyclic code with the generator polynomial g(x) of the form,
Since (n-1)/2=d is the smallest positive integer so that n divide 2d-1, the generator polynomial of the (n, k, d) QR code is irreducible . If the smallest positive integer m so that n|2m-1 is m which is not equal to (n-1)/2, the generator polynomial for this QR code is not irreducible.

## Slide 42: Conceptual Framework
A code polynomial c(x) is a multiple of g(x)
e(x) is a error polynomial has v nozero terms.
where

## Slide 43: Conceptual Framework
known syndromes is obtained by evaluating r(x) at the roots of g(x).
r(x) is a received polynomial.

## Slide 44: Golay Code Using Lookup Table

## Slide 45: Implementation of decoder Using C Code
int De_table[2048];
int beta[23]={ 1, 322, 174, 1164, 1148, 481, 637, 1942, 1887, 1518, 1155, 167, 2011, 418, 281, 1525, 378, 1728, 1747, 319, 552, 1876, 1085 };
void Ge_talbe(){
int Temp = 1; De_table[0]=0;
for (i=0; i< 23; i++) { De_table[Beta[i]]= (Temp <<i;) }
for (i=0; i<21; i++)
for(j=i+1;j<22;j++){
De_table[Beta[i]^Beta[j]]=
((Temp <<i)^(Temp<<j)); } for (i=0; i<20; i++)
for(j=i+1;j<21;j++)
for(k=j+1;k<22;k++){
De_table[Beta[i]^Beta[j] ^Beta[k]]=
((Temp <<i)^(Temp<<j) ^(Temp<<k));
}
int Find_error(int r){
int syndrome;
for(int i=0;i<23;i++)
syndrome=syndrome^De_table[i]*(r>>i)&0x01;
return syndrome;
}
main(){
int c=0; int r;
Ge_table();
r=Addtion_rand_error (c );
c=r^Find_error(r);
}

## Slide 46: (4) Algebraic decoding of some QR Codes
Two QR codes use this scheme decoding of (23, 12, 7) and (47, 24, 11).
Two QR codes have lengths greater than 100.
  (103, 52, 19) QR code
  (113, 57, 15) QR code